## Slide 1: Presentation to The Housing Affordability Commission to study Modular/Industrialized Building Construction
Building Code Commissioner James Cambio
October 16, 2025

## Slide 2: Building Code Regulations
  The primary intent of the state building & fire codes is to protect public health and safety;
Rhode Island, along with the majority of other states across the country, adopt the International Code Council’s (ICC) Model Codes for this purpose;
The Codes with state specific amendments address all aspects of one & two-family dwellings, multifamily dwellings, and commercial buildings.
    structural elements, electrical, plumbing, heating, ventilation and air conditioning systems, and energy conservation requirements;
    requirements that increase wind, snow and hurricane related upgrades to protect against natural disasters

## Slide 3: RISBC-1: Chapter 4 Special Detailed Requirements Based on Occupancy and Use
Section 429 Manufactured Homes.
Manufactured Homes are constructed in accordance with the Federal Department of Housing and Urban Development Part 3280 Manufactured Home Construction and Safety Standards. Refer to Appendix E of the RISBC-2 One and Two-Family Residential Code for specific provisions regarding permitting, foundation systems, additions, site utility connections, and foundation and anchorage details.

## Slide 4: RISBC-1: Chapter 4 Special Detailed Requirements Based on Occupancy and Use
Section 430 Modular Construction
Buildings and structures partially or completely constructed off-site shall be constructed in conformance with this code or the RI Residential One and Two-Family Code (SBC-2) as appropriate for the use and occupancy. Inspection, verification, and approval shall be conducted in accordance with procedures issued by the State Building Code Commissioner.

## Slide 5: Purpose & Administration
Purpose: The purpose of this chapter is to ensure safety to life, health, and property through compliance with uniform statewide construction standards for Industrialized Buildings.
Administration: The Office of the Commissioner is designated as the administrative representative for the registration of industrialized buildings.
Compliance: The Office of the Commissioner will maintain a list of approved compliance assurance agencies and approved manufacturers. Each manufacturer producing industrialized buildings will contract with one or more compliance assurance agencies for required evaluation, quality assurance monitoring, and inspection services.

## Slide 6: Local Building Official Responsibilities
Verify through inspection that the approved industrialized building displays the required state registration seal and the proper label of the compliance assurance agency.
Verify through inspection that the industrialized building has not been damaged in transit to a degree that would render it unsafe.
If warranted due to the nature of any non-compliance issues discovered, the building official shall be permitted to require the correction of any building code issues before occupancy is permitted.
Notify the State administrator of any apparent violations

## Slide 7: Compliance Assurance Agency Certification Label
  1. Modular (Industrialized Buildings) shall be marked with certification labels from the compliance assurance agency that includes the name and address of the agency.
  2. The labels shall be applied to industrialized buildings intended for use in Rhode Island and shall be applied to the building prior to shipment from the place of manufacture.
  3. To the extent practicable, the certification label shall be installed so that it cannot be removed without destroying it. The label shall be applied in the vicinity of the electrical distribution panel or in another location that is readily accessible for inspection.

## Slide 8: Manufacturer’s Data Plate
  All the following information shall be placed on a permanent data plate in the vicinity of the electrical panel or in some other location that is readily accessible for inspection.
  Manufacturer’s name & address
  Compliance Assurance Agency certification number
  Date of Manufacture of the building
  List of codes & standards under which the building was constructed
  Design roof load, design floor live load, design wind speed, and design ground snow load
  Thermal resistance (R-Values) for energy code compliance
  Any special instructions

## Slide 9: Modular Buildings Eligible for State Registration
  Modular buildings must meet all the following requirements to be registered in the state.
  The design of the building has been found by the compliance assurance agency to be in full compliance with the requirements of this code.
  The compliance assurance agency has conducted any necessary testing and evaluation of the building and its component parts.
  The compliance assurance agency has provided the required inspections and other quality assurance follow-up services at the point of manufacture to assure the building complies with this code.
  The building contains the appropriate evidence of such compliance through a label permanently affixed by the compliance assurance agency.

## Slide 10: State of RI Registration Seal
  Modular (Industrialized Buildings) that have met the requirements for shipment to the state shall be marked with the approved registration seal provided by the Office of the Building Code Commissioner.